## Slide 1
Shyam Bhat
VicharaVandana
CAN Error States
AGENDA
Fault Confinement
Error Counters
CAN Error State machine
What is BusOff and how to come out of it.
TEC and REC counter rules

## Slide 2
Guarantees proper network operation even in cases where malfunctioning nodes produce continuous error condition
CAN error detection can pinpoint to “perpetrator”
Distinction between temporary and permanent node failures
Identification and removal (self-retirement) of malfunctioning nodes from the bus
Fault Confinement

## Slide 3
The CAN errors can be classified into Transmit and Receive errors.
Bit error and Acknowledgement error are transmit errors
Reason: These errors can be detected by only transmitting nodes.
CRC error, Form error & stuff error are receive errors
Reason: These errors can be detected by only receiving nodes.
There are 2 counters (count 0 to 255) for each node called error counters namely:
Transmit Error Counter (TEC) : Increments depending on transmit error.
Receive Error Counter (REC) : Increments depending on receive error.
The error counter increment pattern is not simple and depends on many factors as explained in later slides
Error Counters

## Slide 4
Error
Active
Error
Passive
BUS-OFF
TEC > 255
(TEC > 127) or
(REC > 127)
(TEC < 128) AND
(REC < 128)
Reset, Configuration
(Reset, Configuration) Or (Rx 11 consecutive Recessive bits 128 times)
CAN Error State Machine

## Slide 5
REC increments by 1 when receiving node detects an error.
Exception: Detected error was a bit error during transmission of an active error flag or overload flag
REC increments by 8 when Rx node detects a dominant bit after sending an error flag.
REC increments by 8 when Rx node detects a bit error during sending an active error flag or overload flag.
REC increments by 8 if it detects 8 consecutive dominant bits after it sent its error flag.
REC decrements by 1 under following conditions
1. The frame was received properly without any error till ACK slot
2. Successful sending of ACK bit
3. REC is in between 1 and 127
If REC is greather than 127 then its value will be set to a value beterrn 119 and 127.
REC Counter Rules

## Slide 6
TEC will be incremented by 8 when Tx node sends an error flag.
Exception 1: The Tx node is error-passive and detects an ACK error and
doesn't detect a dominant bit while sending passive error flag (bit error).
TEC unchanged.
Exception 2: Tx node sends an error flag due to stuff error during bus
arbitration, where stuff-bit is sent recessive but monitored as dominant.
TEC unchanged.
TEC increments by 8 when Tx node detects a bit error during sending an active error flag or overload flag.
TEC increments by 8 if it detects 8 consecutive dominant bits after it sent its error flag.
TEC decrements by 1 after successful transmission of a frame unless its value is already 0.
TEC Counter Rules